## Slide 1: Exceptional Control Flow
Interrupts, Traps, and Faults

## Slide 2: Review of Standard Control Flow

## Slide 3: What’s in a computer?
Processor
Memory
I/O Devices
Arithmetic Logic Unit
Floating Point Unit
Other Execution Units
Data Registers
Cache
Status (Flag) Registers
Instruction Pointer [IP]
Stack Pointer
[SP]
Frame Pointer
[FP or BP]

## Slide 4: Standard Control Flow
Sequential (execute the next instruction)
Conditional / Unconditional Jumps
  Conditions (“ifs”)
  Loops
Case (Switch) Structures
Procedure Calls

## Slide 5: Procedure Call Review
Backup caller save registers
Place arguments on the stack
call
  Places return address on the stack
  Jumps to beginning of called procedure
Push old FP on the stack and update (FP <= SP)
Backup callee save registers
Put local variables on the stack
run procedure code
Restore callee save registers
Pop the stack (SP <= FP)
Restore original FP
ret
  Jumps to the saved return address
Restore caller save registers
Callee local data
Callee saved registers
Saved FP
Return Address
Passed arguments
Caller saved registers
Callee frame
Caller frame
Low address
High address

## Slide 6: Exceptions
Interrupts, Traps, and Faults

## Slide 7: Q. Why can’t we use procedure calls to give control back to the operating system?
Some events happen asynchronously
Some events are unintentional
We need to switch from user mode to kernel mode

## Slide 8: Types of Exceptions
Type | Sync / Async | Source | Intentional | Examples
Interrupt | Async | External | Yes | I/O Device completion
Trap | Sync | Internal | Yes | System call
Fault* | Sync | Internal | No | Page fault, Overflow, Divide-by-zero, Illegal memory address
* Some texts differentiate between “faults” and “aborts” where a fault may return to the current instruction after being handled, while an abort always results in termination of the program.

## Slide 9: Types of Exceptions
I/O Devices
Processor
Operating System
Application Process
Interrupt
Fault
Trap
New Data
movl $1,%eax
movl $0,%ebx
divl %ebx
int 80
(syscall)

## Slide 10: Simple Exception Handler
Save processor registers;
Execute device code;
Restore processor registers;
Return to original program;
Application
Program
Exception
Handler
exception
return
event

## Slide 11: Exception Handling Issues
What if an event occurs in the middle of executing an instruction?
What if an event occurs while another event is already being handled?
How do we safely return to the original code?
How do we control access to privileged instructions?
What stack to we run exception handlers on?
How do we locate the correct exception handler code?
How do external devices notify the processor of an interrupt?

## Slide 12: Handling Exceptions
Y
Fetch
Decode
Execute
Is Exception?
Run Exception Handler
N

## Slide 13: Disabling Interrupts
Save return address;
Enable interrupts;
Save processor registers;
Execute device code;
Restore processor registers;
Disable interrupts;
Restore return address;
Return to original program;

## Slide 14: The RETI Instruction
We need to safely return to the original code, but cannot re-enable interrupts until after setting the PC.
  RET and JMP instructions are not sufficient!
Solution: Introduce a new instruction – RETI
  Sets the PC to the return address value
  Enables interrupts

## Slide 15: The RETI Instruction
Save return address;
Enable interrupts;
Save processor registers;
Execute device code;
Restore processor registers;
Disable interrupts;
Restore return address;
RETI;

## Slide 16: User and Kernel Modes
User-level processes should not be able to execute certain privileged instructions, nor access certain portions of memory
To enforce this, we introduce a mode:
  User-level processes run in user mode, which is restricted
  The kernel runs in kernel mode, which is unrestricted
Event handlers run in kernel mode
  When an event occurs, we set the mode to kernel mode
How do we ensure that we return to user mode at the finish if and only if the previous context was in user mode?
  Save the current mode before executing the exception handler
  RETI restores the saved mode

## Slide 17: The System Stack
What stack do exception handlers use?
  The exception may not be related to the running process (e.g. hardware interrupt)
Introduce a system stack in the kernel for exception handlers to use
  All kernel code (exception handlers) uses the same system stack
  The system stack has its own stack pointer separate from the user-level SP register
How does it tell which SP to use?
  If in kernel mode, use the system SP register
  Otherwise use the user SP register

## Slide 18: The Interrupt Vector Table
Code or devices raising exceptions do not know the memory address of the exception handler
  However it knows the vector number for its exception type
The interrupt vector table is a map from vector numbers to the memory addresses of the exception handlers
When an exception occurs, the processor looks up the number in the interrupt vector table and executes the exception handler at the stored address

## Slide 19: Interrupt Vector Table Examples
Exception Number | Description | Exception Type
0 | Divide error | Fault
13 | General protection fault | Fault
14 | Page fault | Fault
18 | Machine check | Fault (abort)
32-127 | OS-defined exceptions | Interrupt or Trap
128 (0x80) | System Call | Trap
129-255 | OS-defined exceptions | Interrupt or Trap
These examples are from the Intel-Pentium class architecture.

## Slide 20: Hardware Interrupt Datapath

## Slide 21: Putting It Together – Hardware
Device asserts the INT line
After executing the current instruction, the processor checks the INT line
  Since INT is asserted, the processor asserts the INTA line
Devices pass on the INTA until some device accepts it
That device places its vector number on the data bus

## Slide 22: Putting It Together – Processor INT
Copy the PC to the return address register
Assert INTA
Read vector number from the data bus
Lookup handler address in the interrupt vector table
Copy the handler address to the PC
Save the current mode (user/kernel)
Set the mode to kernel mode
Disable interrupts
Resume execution at the PC
  Which is now set to the exception handler

## Slide 23: Putting It Together – Exception Handler
Save the return address register
Enable interrupts
Save processor registers
Execute device code
Restore processor registers
Disable interrupts
Restore the return address register
RETI

## Slide 24: Putting It Together – RETI
Copy the return address register to the PC
Restore the previous mode (user/kernel)
Enable interrupts